## Slide 1: Kinetic Modeling of Phenol Steam Reforming in a Fixed Bed Reactor - CP302 -Guided by: Dr. Tarak Mondal
Presented by:
Sayed Musaraf Ali
2022CHB1057

## Slide 2: Introduction
Phenol steam reforming (PSR) is a promising route for hydrogen production.
Kinetic modeling is essential for reactor design and optimization.
Why Kinetic Modelling?
  Provides quantitative understanding of reaction rates.
  Essential for reactor design, scale-up, and process optimization.
  Enables comparison of different catalytic systems.

## Slide 3: Project Objectives
Review the kinetics of phenol steam reforming and identify suitable models.
Develop kinetic models for phenol steam reforming in a fixed-bed reactor.
Estimate kinetic parameters from experimental data by different regression techniques.
Validate model using statistical & residual analysis.

## Slide 4: Kinetic Models Considered
Power Law Model :
Arrhenius:
The kinetic model contains 4 parameters (km, Ea, n, m).
This formulation enables parameter estimation by combining partial pressure dependence and temperature dependence.

## Slide 5: Estimation of Kinetic Model Parameters
Power-law rate expression:
Used MATLAB nlinfit, lsqcurvefit, fmincon for regression fitting.
  Multiple Linear Regression (OLS, per temperature)
  Global Linearized Regression (All data together)
  Global Nonlinear Regression
The objective function is:
Minimize
Validate models (R², residuals, confidence intervals).

## Slide 6: Regression Techniques
Multiple Linear Regression (per Temperature)
  Fits the power law form at each temperature separately:
ln(r​) = ln(k) + n.ln(Pph) + m.ln(Pw​)
  Requires a second step (Arrhenius fit) to get activation energy .
Global Linearized Regression (All data together)
  Linearizes the full model including temperature:
  Linearization assumes log-transformed data → may distort error structure.
Global Nonlinear Regression
  Directly fits the nonlinear power law:
  Computationally heavier, sensitive to initial guesses.

## Slide 7: Results Multiple Linear Regression
Estimated Parameters at each Temperature:
From Arrhenius Fit Plot:
Slope = -Ea/R | y-intercept = ln(km)

## Slide 9: Results Global Linear Regression
Estimated Parameters in one shot.

## Slide 10: Results Non-Linear Regression
Optimized parameters (by fmincon):
Parameters | Value
km | 0.15232
Ea | 80 KJ/mol
n | 0
m | 1.87
R2 | 0.6117

## Slide 12: Results Non-Linear Regression
Optimized parameters (by lsqcurvefit):
Parameters | Values | SE
km | 0.07695 | 0.00637
Ea | 46.218 KJ/mol | 1.7822
n | 0.06755 | 0.04712
m | 0.68055 | 0.1785
R2 | 0.9876 | 

## Slide 14: Results Non-Linear Regression
Optimized parameters (by nlinfit):

## Slide 16: Model Validation
Goodness of Fit, R2 = 0.9889

## Slide 17: Model Validation
Goodness of Fit by nlinfit, R2 = 0.9843

## Slide 18: Model Validation
Goodness of Fit, R2 = 0.9876

## Slide 19: Model Validation
Goodness of Fit, R2 = 0.6117

## Slide 20: Error Distributions

## Slide 21: Model Comparison
Global Linear, Non-Linear (nlinfit,lsqcurvefit) are the best fits.
nlinfit is more appropriate that of lsqcurvefit -> More Compact St Error and CI.

## Slide 22: Summary and Conclusion
Successfully estimated Kinetic Parameters using multiple regression techniques.
  Best fits shown for non-linear regression (nlinfit and lsqcurvefit) R2 ~ 0.99
  Provides robust parameter estimation with small uncertainty for km (~0.077), Ea (~46 KJ/mol)
  High uncertainity for reaction orders n (~ 0.06) and m (~ 0.7).
  Overall reaction order (~ 0.8)
Model Validation: Statistical analysis confirms reliability; residuals are random

## Slide 23: LHHW Model Overview
Why go beyond Power Law?
Power-law kinetics is empirical → good statistical fit but no mechanistic insight.
Cannot explain:
  Competitive adsorption
  Surface reaction mechanism
  Product inhibition
  Effect of site coverage
LHHW provides a mechanistic, surface-kinetics-based framework.
Used when:
  Rate-controlling step is surface reaction
  Reactants adsorb on active sites
  Surface coverage influences rate

## Slide 24: LHHW Model
Key Assumptions of LHHW:
  Reaction occurs on active catalyst sites.
  Phenol (P) and Steam (W) adsorb via Langmuir isotherms.
  A single surface-reaction step is rate-controlling.
  No external/internal mass-transfer limitations.
  Catalyst does not deactivate during experiments.
  Ideal-gas behaviour.
We have total of 8 Models (4 Single-site and 4 Dual-sites)
  Both Ph and Steam dissociative.
  Both Ph and Steam non-dissociative.
  Only one dissociative and other non-dissociative and vice-versa.

## Slide 25: LHHW Model
Surface Reaction: C6H5OH + 11H2O ↔ 6CO2 + 14H2
General Rate Expressions:
  SS (Both non-dissociative)
  SS (Both dissociative)
  SS (Phenol dissociative only)
  SS (Steam dissociative only)
  DS (Both non-dissociative)
  DS (Both dissociative)
  DS (Phenol dissociative only)
  DS (Steam dissociative only)
Arrhenius Equation:
Van’t Hoff Adsorption Equation:

## Slide 26: Estimation Technique
Global Nonlinear Regression
15 datapoints (5 experiments × 3 temperatures)
The four unknown parameters from each model:
Minimization of:
MATLAB solver: lsqnonlin (Levenberg–Marquardt)
16 scenarios run:
  4 parameters free
  3 parameters free (×4 combinations)
  2 parameters free (×6 combinations)
  1 parameter free (×4 combinations)
  All fixed
This systematic approach reveals identifiability & parameter correlations.
The thermodynamics consistency verification using Boudart−Mears− Vannice guidelines during parameter estimation.

## Slide 27: Results Table 1 (Arrhenius params)

## Slide 28: Results Table 2 (Adsorption params)
Note: Change in enthalpy written in italics are known from literatures.

## Slide 29: Interpretation of Parameters
Model Selection
  Lowest RMSE obtained for both-dissociative models (SS_both_diss & DS_both_diss ~4.2×10⁻³)
  Indicates that dissociative adsorption of both phenol and steam best represents the reaction mechanism.
Activation Energy (Ea) Trends
  Ea increases in order: both_diss (~97 kJ/mol) < P_diss (~110 kJ/mol) < W_diss (~140 kJ/mol) < nondiss (~157 kJ/mol)
  Lower Ea for both_diss models → more realistic and kinetically favorable pathway.
Pre-exponential Factor (kₘ)
  Dissociative models show lower kₘ values, indicating better mechanistic representation.
Thermodynamic Consistency
  ΔS values are negative for all cases - confirms entropy loss during adsorption.
  Water shows more negative ΔS than phenol - stronger surface interaction of steam.
The reaction is best described by a LHHW mechanism with dissociative adsorption of both phenol and H₂O, followed by surface reaction as the rate-controlling step.

## Slide 30: Parity and Residual Plots

## Slide 31: Parity Plots

## Slide 32: Residual Plots

## Slide 33: Conclusion LHHW Kinetic Modelling
LHHW mechanism applied to PSR kinetics with 8 Model scenarios.
Reason for high errors:
  Strong parameter correlation ( not independent)
  Very small dataset (15 points) → underdetermined 4-parameter model
  Adsorption constants weakly sensitive at experimental conditions
Fully free model gives lowest SSE but unrealistic Eᵢ → overfitting.
Best practical model: LHHW mechanism with dissociative adsorption of both phenol and H₂O.
  Realistic Apparent activation energy (~97 kJ/mol)
  Stable entropic parameters
  Good fit (RMSE ≈ 4.2 E-3)
LMHW model is valid but needs more data + wider operating window for accurate parameter estimation.

## Slide 34: References
https://www.sciencedirect.com/science/article/pii/S0016236122035359
https://www.sciencedirect.com/science/article/pii/S0016236124002485
https://www.sciencedirect.com/science/article/pii/S2213343716303736
https://pubs.acs.org/doi/full/10.1021/ acs.iecr.5b03828
H. Scott Fogler. Elements of Chemical Reaction Engineering. 5th Edition.